## Slide 1
TORCH-SPYRE · PROJECT REVIEW
Bringing State-Space Models
to the Spyre Accelerator
A production Mamba-2 SSD kernel, running fully on-device — the first structured-state-space sequence model on Spyre.
Correctness validated vs. reference · Optimized & profiled on-card · Sequence length up to 32K
IBM
1 / 13

## Slide 2
THE GOAL
Why state-space models matter
Mamba-2 is a leading alternative to the Transformer. It processes long sequences in linear time instead of quadratic — a structural advantage for long-context AI.
▪ Transformer cost grows with the square of sequence length
▪ SSMs stay linear — cheaper as context grows
▪ Used increasingly in frontier long-context & efficiency work
The business case
For Spyre to be a credible platform for modern AI, it must run the architectures customers want to deploy — not only Transformers.
This project proves SSMs run on Spyre, and turns the accelerator's constraints into a concrete backend roadmap.
IBM
2 / 13

## Slide 3
THE CHALLENGE
Spyre is not a GPU
Spyre is a tiled, memory-oriented accelerator. Getting an SSM to run well means respecting hardware rules a GPU never imposes.
▪ Data laid out in 128-byte blocks — every reshape has a cost
▪ No native cumulative-sum, no native attention op
▪ Per-core memory limits bound how big any tensor can be
▪ Half-precision throughout — overflow is a real constraint
The reference is GPU-shaped
The canonical Mamba-2 kernel is written for GPUs: giant fused operations, large chunk size, cumulative-sums everywhere.
None of it maps directly. The work was re-deriving the same math as Spyre-legal operations — and finding where the hardware pushes back.
IBM
3 / 13

## Slide 4
THE APPROACH
Decompose the algorithm into Spyre-legal matmuls
The SSD algorithm splits a long sequence into chunks. Each stage — written as one big operation in the reference — becomes a chain of batched matrix multiplies with the decay folded into the operands.
STAGE 1
Intra-chunk
local mixing within a chunk
→
STAGE 2
Chunk states
summarize each chunk to a state
→
STAGE 3
Inter-chunk scan
carry state across chunks
→
STAGE 4
Combine
merge local + carried into output
Key techniques: cumulative-sum as a matrix multiply · decay folded into operands (no giant intermediate) · half-precision-safe exponentials · fused into one compiled kernel.
Design principle: the kernel is model-agnostic — it computes Y = SSM(X,A,B,C) only, so it is reusable across any SSM.
IBM
4 / 13

## Slide 5
TESTING & VALIDATION
A CPU twin separates “our math” from “the backend”
▪ Reference oracle: the verbatim Mamba-2 kernel on CPU as ground truth
▪ CPU mirror: the same op-sequence as our kernel, in plain PyTorch — pinpoints whether a bug is in our formulation or the hardware
▪ Device-faithful oracle: a half-precision model that predicts Spyre behavior without a compile — so we tune correctness cheaply
Acceptance metric: relative-L2 error < 0.05 — the realistic half-precision budget.
4e-4
fp32 formulation error — math matches reference
9e-4
fp16 numerical floor — best in half precision
0.0038
on-device error at default — near the floor
< 0.05
every validated shape stays within budget
IBM
5 / 13

## Slide 6
ACCOMPLISHMENTS
What works today
100%
On-device — full kernel on Spyre, no CPU fallback in the hot path
32K
Max sequence length validated correct on-card
1
Fused kernel — intra + scan + combine in a single graph
~2×
Kernel speedup from the factored-decay redesign
Fully fused single kernel Accuracy at the fp16 floor Auto-tuned per length Streaming initial-state Safe fallback for large chunks Reusable across SSMs
First structured-state-space model kernel to run on Spyre — from a GPU-only reference to a validated, tuned, on-device implementation.
IBM
6 / 13

## Slide 7
PROFILING
The kernel is memory-bound, not compute-bound
Deep profiling gave the single most important insight of the project: the math is nearly free — moving data is the entire cost.
Ideal compute: ~17 µs
Runtime: milliseconds
Ideal matrix-multiply work is ~17 µs (the compiler's cycle model). The kernel runs orders of magnitude longer — the gap is entirely data movement.
Why this matters strategically
It redirected the entire optimization effort. Chasing compute utilization would have been wasted work.
Every real win came from cutting data movement — fewer layout conversions, smaller intermediates, sharing tensors across ops.
IBM
7 / 13

## Slide 8
OPTIMIZATIONS
Every win cut data movement
▪ Factored decay: fold decay into operands, not a giant matrix — killed a 34 MB intermediate, ~2× faster
▪ Shared layouts: reuse one prepared tensor across two matmuls — measured to the minimum number of conversions
▪ Asymmetric mask build: broadcast one operand in-kernel — halved a 268 MB transfer to 134 MB
▪ Tiling sweep: measured optimal core-tiling on-card — ~34% faster than the previous default
Rigor over intuition
On this hardware, counting operations does not predict speed — a cheaper-looking layout can be slower.
So every change was measured on-device, and several plausible ideas were rejected when the hardware disagreed.
IBM
8 / 13

## Slide 9
OPTIMIZATION · MEASURED
Finding: GPU's chunk size is wrong for Spyre
GPUs use a large chunk size (256). On memory-bound Spyre, the smallest chunk is fastest — the opposite conclusion.
928 ms
chunk 64 (best)
1777 ms
chunk 128
4402 ms
chunk 256 (GPU)
Sequence length 4,096. Lower is faster. Measured on-card.
Why smaller wins
Within-chunk work grows with the square of chunk size. Because the kernel is memory-bound, that intermediate dominates — the smallest legal chunk moves the least data.
Takeaway: hardware-specific tuning beats porting GPU defaults.
IBM
9 / 13

## Slide 10
LONG-CONTEXT ENVELOPE
Correct & running up to 32K tokens
0.0039
4K
0.0047
8K
0.0057
16K
0.0109
32K
✗
64K
Green = validated on-device. Budget = 0.05. Bars scaled to budget.
The maximum sequence length doubled this cycle — from 16K to 32K — by re-measuring a hardware limit against the latest backend.
▪ Each length uses its own measured-best chunk size
▪ Error stays within budget across the whole range
▪ 64K+ is blocked by a specific, identified backend limitation — not by our math
IBM
10 / 13

## Slide 11
FUTURE WORK
One backend fix unlocks the next frontier
Beyond 32K, one tensor grows past the per-core memory limit. The algorithmic fix is known and CPU-validated — it needs one backend capability.
▪ Sub-quadratic scan — validated correct on CPU; the math is ready
▪ The blocker: reshaping a tensor into blocks corrupts its layout on-device
▪ The ask: correct layout across a splitting reshape — one well-scoped capability
Turning a kernel into a roadmap
This project produced a prioritized list of backend capabilities, each with a minimal reproducer and a clear payoff:
▪ Splitting-reshape layout → unlocks 64K+
▪ On-chip residency → cuts the memory tax
▪ Layout-sharing across ops → general speedup
IBM
11 / 13

## Slide 12
IMPACT & LONG-TERM GOAL
From one kernel to a platform capability
Impact today
▪ SSMs are proven viable on Spyre
▪ A validated, tuned, reusable kernel others build on
▪ A concrete, evidence-backed backend roadmap
Long-term goal
▪ Full Mamba-2 layer — projections, conv, norm, decode
▪ End-to-end SSM inference for long-context serving
▪ Backend fixes that speed up the whole platform
DONE
SSD core kernel
on-device, tuned, 32K
→
NEXT
Full layer
proj · conv · norm · gate
→
THEN
Decode step
recurrent inference
→
GOAL
SSM serving
long-context, on Spyre
IBM
12 / 13

## Slide 13
SUMMARY
SSMs run on Spyre —
correct, tuned, up to 32K.
We took a GPU-only architecture, re-derived it for Spyre's constraints, validated it to the precision floor, and optimized it to its memory-bound ceiling.
The path to full SSM serving is clear — and the backend work it needs is identified, reproduced, and prioritized.
Thank you · Questions welcome
IBM
13 / 13